## Slide 1
Microprocessor
Instruction Size

## Slide 2
Introduction
When we give the instructions in 8085, it gets stored in memory location.
The total memory location required to feed the instruction in memory is called instruction word size.
The memory location of 8085 microprocessor can accommodate 8 bits of data. So the length is measured in terms of “byte” rather than “word” as 8085 has 8 bit data bus
To store 16 bits of data, they are stored in two consecutive memory locations.
The 8085 instruction set is classified into 3 categories according to the lenght of the instructions. They are:
- 1-byte instruction
- 2-byte instruction
` - 3-byte instruction

## Slide 3
Introduction
1-byte instruction:
In 1-byte instruction, the opcode and operand of an instruction are represented in one byte.
In this, opcode and operand are included in the same byte.
Operands are internal registers and coded into instruction.
Instructions require one memory location to store the single byte in the memory.
Instruction having only register or register pair as operand is 1 byte instruction.
If operand is absent then those instructions are also 1 byte instruction.
Example:
  MOV B, C
  LDAX B
  NOP
  HLT

## Slide 4
Introduction
2-byte instruction:
Two byte instruction is the type of instruction in which first 8 bits indicates the opcode and next 8 bits indicates the operand.
It requires two memory locations to store in the memory.
Instruction having 8 bit number either as an address or data as the operand is 2 – byte instructions.
Example:
  MVI B, 26h
  IN 56h

## Slide 5
Introduction
3-byte instruction:
In three byte instruction, the first byte specifies the opcode, and the following two bytes specify the 16 bit address.
The 2nd byte holds the low order address.
The 3rd byte holds the high order address.
3 byte instruction require three memory location to store the single instruction the memory.
Instruction having 16 bit number either as an address or data as the operand is 3 – byte instructions.
Example:
  LDA 2050H
  JMP 2085H